## Slide 1: Indoor Passive Bistatic Radar using WiFi
Alexander Tooke and Ernest Carozza

## Slide 2: Introduction and Motivation
Indoor localization has many applications
  Supplement to GPS in absence of line of sight to satellites
  Tracking equipment in factory
  Search and rescue
  Law enforcement
WiFi is widely used in homes and offices, transmissions reflecting off walls, furniture, people all the time
Analyzing fading can lead to information about objects’ position and movement
Notes: Aim for 1 minute

## Slide 3: Problem Statement
Is it feasible to detect the position and speed of a uncooperative target inside a building using signals from an existing WiFi network?
Assumptions:
  Transmitter (WiFi router) position known
  Transmitter using 802.11g based on OFDM at 2.4GHz
Main idea: apply radar techniques and understanding of wireless communication protocols
TODO radar formulas
Notes: Aim for 2 minutes
Precise definitions
Formulas/mathematical models
Specific goal

## Slide 4: Approach
Develop a simulation of indoor fading with walls and a moving target
  Receiver sees not only the transmissions from the router but also reflections of the moving target
  How does the channel change as the target moves?
  TODO more mathematical description
Simulate OFDM transmissions over the channel
  All 802.11g data rates
  Assume OFDM symbols constantly transmitted
Use radar techniques to correlate transmitted and received signal
Notes: Aim for 3 minutes
Main ideas used to tackle the problem
Key equations

## Slide 5: Simulating the Indoor Channel
Develop a ray tracing simulation to estimate the impulse response
Simplifications:
  Consider single floor building with no reflection from ceiling or floor
  Walls both reflect some energy and transmit some energy
  A moving target also reflects and transmits some energy
Techniques based on “A graphical indoor radio channel simulator using 2D ray tracing” by Holt and Pahlavan
Intuition: As distance to target changes, the subset of taps from reflections of target will shift
Notes: Aim for 1-2 minutes
Why were these simulations chosen?
Clear descriptions of parameter choices
Discuss what the plots mean
Do the plots match the papers? If not, why?

## Slide 6: Simulating the Indoor Channel
TODO pictures

## Slide 7: Forming Range-Doppler Maps
RDMs are ………..
Notes: Aim for 1-2 minutes
Why were these simulations chosen?
Clear descriptions of parameter choices
Discuss what the plots mean
Do the plots match the papers? If not, why?

## Slide 8: Conclusion
Notes: Aim for 1 minute